"097" Duntov Cam

The original "097" Duntov was used from late 1956 to 1963 and designed for 0.012-0.018-inch clearance with 1.5:1 rocker arms. But in 1963 the intake clearance was revised to 0.008-inch and this change was also recommended in Corvette News in the late 1950's for "weekend competition events"; the tighter intake clearance gave a bit more effective inlet duration. Factoring the original 0.012-0.018-inch by the 1.37/1.50 rocker ratio correction yields 0.01096-0.01644-inch, call it 0.011-0.016-inch (hot), so if you're already running the 0.008-inch intake clearance it shouldn't be tightened any further. We recommend a (cold) setting of 0.010-inch intake and 0.015-inch exhaust for 283s, and 0.008-inch intake and 0.015-inch exhaust for 327s. A complete crank angle/cam lift diagram in Corvette News, Vol.8, No.4, indicates that neither the exhaust nor the inlet is on the clearance ramp at TDC of the firing stroke, so you can use the indexing procedure outlined earlier, or it's also OK to adjust both the inlet and exhaust at TDC #1 and TDC #6 as outlined in the 1963 Corvette Shop Manual with the "097" Duntov cam; it has much shorter ramps than the "30-30" or the LT-1 cam.

http://www.centuryperformance.com/valveadjustment.asp

Method #1:  For a small block Chevy (or any engine with a firing order of 18436572) you can set the valves by turning the engine over just two times. Bring the engine up to #1 firing (both #1 valves closed and the timing mark aligned with zero on the timing tab) and adjust as follows: exhaust valves 1,3,4,8 and intake valves 1,2,5,7 bring engine up to #6 firing(rotate engine one complete revolution) and adjust as follows: exhaust valves 2,5,6,7 and intake valves 3,4,6,8.

The smallest MECHANICAL I can find in my catalogs is either the early 097 duntov cam.

ADV Duration : intake 287° / exhaust 287° 
Duration .050” : intake 228° / exhaust 230° 
Valve Lift Inches : intake .395 / exhaust .401 
Degrees Lobe Centerline: intake 108° / exhaust 112° 
Valve Lash Intake .012"/ exhaust .018" 

or Clevite 229-1998 

ADV Duration : intake 257° / exhaust 269° 
Duration .050” : intake 218° / exhaust 228° 
Valve Lift Inches : intake .459 / exhaust .479 
Degrees Lobe Centerline: intake 110° / exhaust 118° 
Valve Lash Intake .022"/ exhaust .022"

Chevrolet Small Block 267/283/305/327/350/400

Clockwise Distributor Rotation: 1-8-4-3-6-5-7-2