- Chock wheels.

- Disconnect EST. (brown wire/black tracing into black connector – see photo)

- Start engine, put in Neutral for manual transmission; Drive for automatic.

- Set timing to 6 degrees BTDC. (large notch is 0o; each additional notch is 2o increment – see photo)

- Lock down distributor....re- check timing again to be sure you didn't move distributor when locking it down.

- Shut off engine.

- Plug in EST.

- Disconnect battery to remove code...wait 10-30 seconds....re-connect battery.

- Good to go.