How to Tune the F55 Magnetic Selective Ride Shocks Out of the C5

Submitted by 8VETTE7 on CorvetteForum.com.  (7/27/10)

You can look on the inside of the glove box door and look for RPO code F55. If you have that RPO then it is Magnetic Ride Control. From a dealer you are probably looking at a cost of $3600 or more. Each shock lists at about $900. From Gene Culley (GMPARTSHOUSE.COM) you can buy them for about $600 each. Significant savings but for my money STILL WAY WAY too much for shocks no matter how good they are claimed to be.

If you can find some one with a TECH II you can bypass the F55 option in the car and then run C6Z06 shocks which you can buy from Gene at $240 FOR ALL four shocks.

Here is the information about bypassing the F55 option with a Tech II:

1. Hook up your Tech II (Driver's foot well), turn the car ON, make sure the module in the left rear storage compartment (pull back the velcro lining on the front of the compartment) is plugged in. DO NOT UNPLUG THIS MODULE.

2. Now use the Tech II to delete the F45 option (F55 option does not appear on the Tech II menu screen - SO - DELETE THE F45 OPTION.
(use the screen captures - steps 2-14)

3. Save the new configuration

4. DO NOT TURN THE CAR OFF AND DO NOT REMOVE THE TECH II.  Go to the module in the rear of the car, unplug the GRAY connector - IT IS THE WIDEST ONE - leave the other 1 (F/45) or 2 (F/55) plugged in.

5. Turn off the car but LEAVE THE TECH II PLUGGED IN.

6. Remove remaining plugs from module in the rear of the car - Never plug them back in again, if you do the F/45 turns on automatically.

7. Now the moment of TRUTH - Turn the car on and verify that the dreaded - MAX SPEED 80 MPH - is gone. This message was only present if you had already disconnected the shock sensors. Some people have had to disconnect their battery to allow the computer to reset to remove this message, but I would confirm with the Tech II that the F/45 was actually deleted first and if not reconnect everything and start again with step 1.

8. Unplug the Tech II - Get in the car and take it for a ride. Smile as you pass the DREADED 80 MPH.

With these instructions in their hands even the most inexperienced technician can do this. It took mine five minutes and they charged me $25. I would have spent much more time and effort getting and installing resistors.

If you haven't already changed your shocks drive home carefully as the shocks become very soft, not dangerous but as GM advises keep it under 80MPH.


You may get some posters that will tell you can use "simulators or resistors to fool the system. These work on the earlier F45 suspension for the 2002 and earlier cars. It does not work for the F55 suspension.